## Slide 1
Welcome Asbestos – Best Rcommended Practice and Regulatory Requirements Webinar will begin at 10:30am Presented by: Daniel J. Larson, MS., CIH Pennsylvania OSHA Consultation Office Phone: 724-357-4095 Website: www.iup.edu/pa-oshaconsultation

## Slide 2: Asbestos – Best Recommended Practice & Regulatory Requirements
Webinar General Info PowerPoint Presentation Q&A Questions Chat is open to submit questions. We will be answering questions through this chat feature. If due to the technical nature of the question a more thorough response is required, we will post the answer on our website within seven days of the webinar.
www.iup.edu/pa-oshaconsultation

## Slide 3: Asbestos - Background
Asbestos. What is it?
Asbestos is a naturally occurring group of minerals that can only be identified under a microscope. There are several types of these flexible, fire-resistant fibers.
www.iup.edu/pa-oshaconsultation

## Slide 4: Asbestos - Background
Ancient Greeks and Romans used asbestos woven into cloth or other materials similar to cotton.
It was not available in large amounts until extensive deposits were discovered in Canada in the nineteenth century (late 1800’s).
Following this discovery, asbestos emerged as an insulating component in thermal insulation for boilers, pipes and other high temperature applications and as a reinforcement material for a variety of products.

## Slide 5: Asbestos - Backgound
Three Major Types of Asbestos:
Chrysotile is the most commonly used type of asbestos and accounts for approximately 95% of the asbestos found in buildings in the United States. Chrysotile is commonly known as "white asbestos" or named for its natural color.
www.iup.edu/pa-oshaconsultation

## Slide 6: Asbestos - Background
Amosite is the second most likely type to be found in buildings, is often referred to as "brown asbestos". As you might assume, in its natural state amosite is brown in color.
www.iup.edu/pa-oshaconsultation

## Slide 7: Asbestos - Background
Crocidolite, "blue asbestos" is also an amphibole. Crocidolite was used in high temperature insulation applications.
www.iup.edu/pa-oshaconsultation

## Slide 8: Asbestos - Background
Why was asbestos used?
For many years, asbestos was called the magic mineral because of its unique nature and widespread usefulness. The word itself comes from the Greek word for incombustible. The mineral's fire-retardant qualities are among its most valuable characteristics. This led to its wide use in ships, buildings and theater curtains, where protection against fire was essential.
In addition to its fire-retardant properties, it has other qualities which make it useful, including: a fibrous nature, heat stability, thermal and electrical resistance, flexibility, high tensile strength and stability in acids or alkalis, Untold thousands of lives have been saved by the use of asbestos.
www.iup.edu/pa-oshaconsultation

## Slide 9: Asbestos - Background
How widely was asbestos used in the United States?
Asbestos has been used extensively. Asbestos consumption jumped dramatically in the United States during World War II, because of the Navy's determination that it was an essential component of shipboard fire protection.
Up until 1976, it was required by model building codes in specific areas of buildings where protection against fire was essential. In 1973 and again in 1978, however, the EPA prohibited certain spraying of asbestos-containing materials as part of its air pollution regulations.
www.iup.edu/pa-oshaconsultation

## Slide 10: Asbestos - Background
Is asbestos still used in the United States?
It is still possible to purchase building materials containing asbestos. Therefore, it is very important to specify non-asbestos containing materials when ordering building materials.
Two definitions to be aware of:
  Friable – Asbestos that can be crumbled to a powder in your hand. This is the most dangerous type of asbestos because it can easily become airborne and inhaled or ingested.
  Nonfriable – Cannot be readily crumbled to a powder. Example – Vinyl floor tile.
www.iup.edu/pa-oshaconsultation

## Slide 11: Asbestos – Examples of Use
ACOUSTICAL SOUND PLASTER

## Slide 12: Asbestos – Examples of Use
Acoustical (Sound) Tiles

## Slide 13: Asbestos – Examples of Use
Blackboard Mastic

## Slide 14: Asbestos – Examples of Use
Boiler Insulation

## Slide 15: Asbestos – Examples of Use
Brake Shoes

## Slide 16: Asbestos – Examples of Use
Ceiling Insulation

## Slide 17: Asbestos – Examples of Use
Ceiling Tiles and Ceiling Tile Mastic

## Slide 18: Asbestos – Examples of Use
Tank Insulation

## Slide 19: Asbestos – Examples of Use
Decorative Plaster

## Slide 20: Asbestos – Examples of Use
Door & Window Caulking

## Slide 21: Asbestos – Examples of Use
Drywall & Joint Compound

## Slide 22: Asbestos – Examples of Use
Duct Insulation

## Slide 23: Asbestos – Examples of Use
Electrical Insulation

## Slide 24: Asbestos – Examples of Use
Exterior Building Siding

## Slide 25: Asbestos – Examples of Use
Fire Blankets

## Slide 26: Asbestos – Examples of Use
Fire Curtains

## Slide 27
Fire Doors

## Slide 28: Asbestos – Examples of Use
Fireproofing on Beams

## Slide 29: Asbestos – Examples of Use
Flue Pipes

## Slide 30: Asbestos – Examples of Use
Mastic

## Slide 31: Asbestos – Examples of Use
Pipe Gaskets

## Slide 32
Pipe Insulation

## Slide 33: Asbestos – Examples of Use
Roofing Felts & Shingles

## Slide 34: Asbestos – Examples of Use
Roofing Asphalt

## Slide 35: Asbestos – Examples of Use
Thermal Tape And Expansion Cloth or Vibration Dampener

## Slide 36: Asbestos – Examples of Use
Transite (Cement-type) Sheets

## Slide 37: Asbestos – Examples of Use
Transite (Cement-type) Pipes

## Slide 38: Asbestos – Examples of Use
Vinyl-Asbestos Floor Tiles

## Slide 39: Asbestos – Examples of Use
Wall and Ceiling Plasters

## Slide 40: Asbestos – Examples of Use
Window Glazing

## Slide 41: Asbestos – Health Effects
ASBESTOS DISEASE Key Facts
Asbestos can kill you unless you protect yourself.
Asbestos is silent and deadly. You do not know it is there. You cannot see, hear, feel, taste, smell, or touch the small asbestos fibers that enter your body. When asbestos is in the air, it gets into your body when you breathe and when you swallow.

## Slide 42: Asbestos – Health Effects
Diseases
Asbestos causes four types of disease:
Asbestosis, “white lung”- a scarring of the lungs which makes it hard to breathe.
Mesothelioma, the “marker disease” – a cancer of the lining of the lungs or the lining of the abdomen. It is very rare but is typically fatal. It is not dose-related.

## Slide 43: Asbestos – Health Effects
Lung Cancer (also caused by smoking) is the biggest killer of all the asbestos diseases. Asbestos workers who smoke are 80 times more likely to get lung cancer than the general public.
Other Cancers- cancers of the stomach, etc.

## Slide 44: Asbestos – Health Effects
Dose-Related
The more asbestos fibers you breathe or swallow, the more likely you are to get sick. This is called a dose relationship. The higher the amount of asbestos, the greater your chances of getting an asbestos disease. Mesothelioma is the exception.

## Slide 45: Asbestos – Health Effects
Latency Period
All of the asbestos diseases have a latency period. The latency period is the time gap between when you take the asbestos into your body and when you become sick. For asbestos diseases the latency period is between 10 to 40 years long.

## Slide 46: Asbestos – Best Recommended Practices
How To Manage Asbestos

## Slide 47: Asbestos – Best Recommended Practices
If the asbestos material is in good shape and will not be disturbed, do nothing!

## Slide 48: Asbestos – Best Recommended Practices
If it is a problem or if it is going to be disturbed by renovation or demolition activities, there are two types of corrections: repair and removal. These activities must be performed by a professional trained and certified/licensed to handle asbestos safely.

## Slide 49: Asbestos – Best Recommended Practices
REPAIR usually involves either sealing or covering asbestos material.

## Slide 50: Asbestos – Best Recommended Practices
SEALING (encapsulation) involves treating the material with a sealant that either binds the asbestos fibers together or coats the material so fibers are not released. Pipe, furnace, and boiler insulation can sometimes be repaired this way.

## Slide 51: Asbestos – Best Recommended Practices
COVERING (enclosure) involves placing something over or around the material that contains asbestos to prevent release of fibers. Exposed insulated piping may be covered with a protective wrap or jacket.

## Slide 52: Asbestos – Best Recommended Practices
With any type of repair, the asbestos remains in place. Repair is usually cheaper than removal, but it may make later removal of asbestos, if necessary, more difficult and costly.

## Slide 53: Asbestos – Best Recommended Practices
All of this work requires that the work area be segregated/contained to prevent asbestos fibers from being released into the rest of the building or into the outside environment.

## Slide 54: Asbestos – Best Recommended Practices
The trained and certified/licensed workers performing the work must wear protective clothing and respirators designed for asbestos work.

## Slide 55: Asbestos – Regulatory Requirements – General Industry 1910.1001
a) Scope and application: Applies to all occupational exposures except for construction and shipyard activities.
b) Definitions (Key Ones)
  Asbestos – Includes all types (e.g., chrysotile, amosite, crocidolite, etc.)
  Asbestos-containing material – Any material greater than 1% asbestos. This is an important definition.
c) Permissible Exposure Limit
  0.1 f/cc as a 8-hour time weighted average (TWA)
  1.0 f/cc excursion limit over a 30-minute period
d) Exposure monitoring
  Must determine TWA exposures by personal air monitoring
www.iup.edu/pa-oshaconsultation

## Slide 56: Asbestos – Regulatory Requirements – General Industry 1910.1001
e) Regulated area:
  Required where airborne exposures exceed the TWA or Excursion Limit
  Demarcation – Regulated areas must be posted
  Access must be limited
  Respirators required
f) Methods of compliance:
  Utilize engineering controls and work practices to maintain employee exposure below the TWA and Excursion Limit when feasible
  When engineering controls and work practices do not maintain employee exposures below TWA and Excursion Limit supplement with PPE (e.g., respirators).
  Utilize wet methods when practicable
  Do not use compressed air (unless used with local exhaust ventilation)
  Implement a written compliance program in areas where exposure exceeds TWA or Excursion Limit
  Brake/clutch repair – Utilize HEPA vacuum system or wet methods
www.iup.edu/pa-oshaconsultation

## Slide 57: Asbestos – Regulatory Requirements – General Industry 1910.1001
g) Respirators:
  Approved respirators must be provided in areas respirators are required
  Must implement a full Respiratory Protection Program as per 1910.134
h) Protective clothing and equipment:
  If employee exposures are above TWA and/or Excursion Limit coveralls, gloves, head coverings, foot coverings, face shields, eye protection is required
  Contaminated work clothing must be removed in approved change rooms and properly laundered
i) Hygiene facilities:
  Change rooms required if employee exposures are above TWA and/or Excursion Limit
  Shower facilities required if employee exposures are above TWA and/or Excursion Limit
  Separate lunchrooms must be provided if employee exposures are above TWA and/or Excursion Limit
www.iup.edu/pa-oshaconsultation

## Slide 58: Asbestos – Regulatory Requirements – General Industry 1910.1001
j) Communication of hazards to employees:
  Include asbestos in employee hazard communication program
  Building and facility owners must determine the presence, location and quantity of asbestos at the work site
  Utilize appropriate warning labels and signs
k) Housekeeping:
  Surfaces shall be maintained as free as practicable of ACM waste and dust
  Spills and sudden releases shall be cleaned up as soon as possible
  Utilize HEPA vacuum for cleaning purposes
  Do not utilized compressed air to clean surfaces
l) Medical surveillance:
  Required if employee exposures are above TWA and/or Excursion Limit
  Includes: pre-placement exam, periodic exam, medical testing
www.iup.edu/pa-oshaconsultation

## Slide 59: Asbestos – Regulatory Requirements – General Industry 1910.1001
m) Recordkeeping
  Maintain employee exposure records for at least 30 years
  Maintain employee medical records for at least 30 years
n) Observation of monitoring
  Must provide employee or their representative the opportunity to observe any monitoring
www.iup.edu/pa-oshaconsultation

## Slide 60: Asbestos – Regulatory Requirements – Construction – 1926.1101
a) Scope – This regulation applies to:
  Demolition or salvage of structures
  Removal or encapsulation of materials containing asbestos
  Construction, alteration, repair, maintenance or renovation of structures, substrates or portions thereof that contain asbestos
  Installation of products that contain asbestos
  Asbestos spill/emergency clean up
  This section does not apply to asbestos containing, asphalt roof coatings, cements and mastics
www.iup.edu/pa-oshaconsultation

## Slide 61: Asbestos – Regulatory Requirements – Construction – 1926.1101
b) Definitions
  Asbestos-containing material (ACM) – Any material containing greater than 1% asbestos
  Class 1 asbestos work – Removal of TSI and surfacing ACM and PACM
  Class 2 asbestos work – Removal of ACM which is not TSI or surfacing material. Examples: wallboard, floor tile, sheeting, roofing, siding shingles, construction mastics
  Class 3 asbestos work – Repair and maintenance operations
  Class 4 asbestos work – Maintenance and custodial activities during which employees contact but do not disturb ACM
  Competent person – Person who can identify asbestos hazards, select appropriate controls, has authority to take corrective action. For class 1 and 2 work must receive EPA training.
  Regulated Area – Area where class 1, 2 or 3 asbestos work occurs
www.iup.edu/pa-oshaconsultation

## Slide 62: Asbestos – Regulatory Requirements – Construction – 1926.1101
c) Permissible Exposure Limit
  0.1 f/cc as a 8-hour time weighted average (TWA)
  1.0 f/cc excursion limit over a 30-minute period
d) Multi-employer worksites
  Must notify other employees on the site of asbestos activities
  General contractor for site must ensure compliance with standard
e) Regulated areas
  Required in Class 1, 2 or 3 work and where airborne exposures exceed the TWA or Excursion Limit
  Demarcation – Regulated areas must be posted
  Access must be limited
  Respirators required
www.iup.edu/pa-oshaconsultation

## Slide 63: Asbestos – Regulatory Requirements – Construction – 1926.1101
f) Exposure assessment:
  Competent person must conduct or direct exposure assessment to evaluate employee exposure
  Negative exposure assessment – Assessment demonstrates exposure does not exceed TWA or Excursion Limits
  Periodic monitoring:
    Class 1 and 2 Work – Daily monitoring required
    Other than class 1 and 2 work – Periodic monitoring required
    Notify employees of results withing 5 working days
www.iup.edu/pa-oshaconsultation

## Slide 64: Asbestos – Regulatory Requirements – Construction – 1926.1101
g) Methods of compliance – Major Points
  Required engineering and work practice controls
  Wet methods, HEPA vacuums and prompt clean up/disposal of wastes and debris
  Negative pressure containment with 4 air changes/hour
  Critical barriers
  Isolation of HVAC systems
  Materials inside containment covered with plastic/impermeable drop cloth
  Prohibitions – High speed disc saws (w/no HEPA filtration), use of compressed air, dry sweeping or dry clean up of ACM
www.iup.edu/pa-oshaconsultation

## Slide 65: Asbestos – Regulatory Requirements – Construction – 1926.1101
g) Methods of compliance – Major Points/Requirements
  Required engineering and work practice controls
  Wet methods, HEPA vacuums and prompt clean up/disposal of wastes and debris
  Negative pressure containment with 4 air changes/hour
  Critical barriers
  Isolation of HVAC systems
  Materials inside containment covered with plastic/impermeable drop cloth
  Prohibited – High speed disc saws (w/no HEPA filtration), use of compressed air, dry sweeping or dry clean up of ACM
  See EPA Model Curriculum for all requirements such as worker, supervisor training requirements.
www.iup.edu/pa-oshaconsultation

## Slide 66: Asbestos – Regulatory Requirements – Construction – 1926.1101
h) Respiratory protection
  Employer must provide approved respirator
  Respirators required:
    Class 1 work
    Class 2 work – when ACM not removed substantially intact
    Class 2 and 3 work – when wet methods not utilized or when a negative exposure assessment has not been completed
    Class 3 work – when TSI or surfacing ACM or PACM is disturbed
    Any occasion employees are required to be inside a regulated area (e.g., to perform custodial duties)
    Any occasion employees are exposed above the TWA or Excursion Limit
  Must implement a respiratory protection program in compliance with 1910.134.
www.iup.edu/pa-oshaconsultation

## Slide 67: Asbestos – Regulatory Requirements – Construction – 1926.1101
i) Protective clothing – During class 1 work, or if employee exposures are above TWA and/or Excursion Limit or if no negative exposure assessment has been conducted:
  Coveralls, gloves, head coverings, etc. required
  Protective clothing must be regularly inspected
  Contaminated work clothing must be removed properly, bagged in impermeable containers and properly labeled
j) Hygiene facilities – Required for class 1 work
  Three (3) stage decontamination area required attached to regulated area
    Equipment Room/Shower Area/Clean Change Room
  No smoking permitted in work areas
www.iup.edu/pa-oshaconsultation

## Slide 68: Asbestos – Regulatory Requirements – Construction – 1926.1101
k) Communication of hazards to employees:
  Include asbestos in employee hazard communication program
  Building and facility owners must determine the presence, location and quantity of asbestos at the work site
  Utilize appropriate warning labels and signs
l) Housekeeping:
  Utilize HEPA vacuums
  Asbestos waste, debris, etc. must be collected and disposed of in sealed, labeled, impermeable bags/containers
  Asbestos waste and debris shall be promptly cleaned up and disposed of in leak tight containers
www.iup.edu/pa-oshaconsultation

## Slide 69: Asbestos – Regulatory Requirements – Construction – 1926.1101
m) Medical surveillance:
  Required if employees perform class 1, 2 and 3 work for 30 or more days per year
  Required if employee exposures are above TWA and/or Excursion Limit for 30 or more days per year
  Includes: pre-placement exam, periodic exam, medical testing
n) Recordkeeping
  Maintain employee exposure records for at least 30 years
  Maintain employee medical records for at least 30 years
o) Competent Person
  Required on each job site to ensure worker safety and health
  Performs frequent and regular inspections
www.iup.edu/pa-oshaconsultation

## Slide 70: Asbestos – Other Regulatory Requirements - AHERA
Asbestos Hazard Emergency Response Act – Asbestos-Containing Materials In Schools (AHERA) – Part III 40 CFR Part 763
  Regulates asbestos in public and private Kindergarten through 12th grade schools.
  Enforced by EPA
  Requires inspections to determine presence of asbestos-containing materials and the development of asbestos management plans
www.iup.edu/pa-oshaconsultation

## Slide 71: Asbestos – Other Regulatory Requirements - NESHAP
National Emission Standards for Hazardous Air Pollutants (NESHAP) – 40 CFR 61 Subpart M.
  Protects people and the environment
  Enforced by EPA
  Requires inspections to determine presence of asbestos-containing materials prior to demolition activity
  “No visible emission of asbestos”
  EPA and PA notification requirements
www.iup.edu/pa-oshaconsultation

## Slide 72: Heading
Add Text
www.iup.edu/pa-oshaconsultation

## Slide 73: Heading
Add Text
www.iup.edu/pa-oshaconsultation

## Slide 74
www.iup.edu/pa-oshaconsultation
www.iup.edu/pa-oshaconsultation

## Slide 75
www.iup.edu/pa-oshaconsultation
Please consider subscribing to our youtube channel to be notified of new webinars: https://www.youtube.com/@paoshaconsultationpaosha2922

## Slide 76: Contact us
Consultant Name
Email
Pennsylvania OSHA Consultation Office
Phone: 724-357-4095
Website: www.iup.edu/pa-oshaconsultation/
Facebook: https://www.facebook.com/Pennsylvania-OSHA-Consultation-Program-548810235234647/
Twitter: https://twitter.com/search?q=PA%20OSHA%20Consultation&src=savs
www.iup.edu/pa-oshaconsultation

## Slide 77: Thank You
Upcoming Webinar:
LIST TOPIC HERE
LIST DATE HERE@ 10:30am
Pennsylvania OSHA Consultation Office
Phone: 724-357-4095
Website: www.iup.edu/pa-oshaconsultation
www.iup.edu/pa-oshaconsultation