## Slide 1
Welcome OSHA’s Respiratory Protection Standard 29 CFR 1910.134 Will begin at 10:30am Presented by: Bryan Brougher, CSP Pennsylvania OSHA Consultation Office Phone: 800-382-1241 or 724-357-4095 Website: www.iup.edu/pa-oshaconsultation

## Slide 2: OSHA’s Respiratory Protection Standard 29 CFR 1910.134
Webinar General Info PowerPoint Presentation Q&A Questions Chat is open to submit questions. We will be answering questions through this chat feature. If due to the technical nature of the question a more thorough response is required, we will post the answer on our website within seven days of the webinar.
www.iup.edu/pa-oshaconsultation

## Slide 3: Scope
General Industry (Part 1910),
Shipyards (Part 1915),
Marine Terminals (Part 1917),
Longshoring (Part 1918), and
Construction (Part 1926).
This standard applies to:

## Slide 4: Scope
Respirator-related provisions of OSHA’s existing standards are revised to conform to each other and covered in 29 CFR 1910.134
All provisions addressing respirator use, selection, and fit testing are deleted from OSHA’s substance-specific standards
Revisions to Specific OSHA Standards

## Slide 5: Organization of Standard
(a) Permissible practice
(b) Definitions
(c) Respirator program
(d) Selection of respirators
(e) Medical evaluation
(f) Fit testing
(g) Use of respirators
(h) Maintenance and care
(i) Breathing air quality and use
(j) Identification of filters, cartridges, and canisters

## Slide 6: Organization of Standard
B-1: User Seal Checks
B-2: Cleaning Procedures
C: Medical Questionnaire
D: Information for Employees Wearing Respirators When Not Required Under the Standard
(k) Training and information
(l) Program evaluation
(m) Recordkeeping
(n) Dates
(o) Appendices (mandatory)
A: Fit Testing Procedures

## Slide 7: Permissible Practice
The primary means to control - feasible engineering controls
Not feasible or while being instituted - Respiratory protection
Employer provided respirators - applicable and suitable
Employer responsible for establishment and maintenance of a respirator program

## Slide 8: Definitions
Employee Exposure
Exposure to a concentration of an airborne contaminant that would occur if the employee were not using respiratory protection.

## Slide 9
Respiratory Inlet Covering
Portion of respirator that forms the protective barrier between user’s respiratory tract and an air-purifying device or breathing air source, or both.
Definitions

## Slide 10: Tight-Fitting Coverings
Quarter Mask
Half Mask
Full Facepiece
Mouthpiece/Nose Clamp
(no fit test required)

## Slide 11: Loose-Fitting Coverings
Hood
Helmet
Loose-Fitting
Facepiece
Full Body Suit

## Slide 12: Definitions
Filter or air purifying element
A component used in respirators to remove solid or liquid aerosols from the inspired air.

## Slide 13: Definitions
Canister or Cartridge
A container with a filter, sorbent, or catalyst, or combination of these items, which removes specific contaminants from the air passed through the container.

## Slide 14: Definitions
Negative Pressure Respirator
A respirator in which the air pressure inside the facepiece is negative during inhalation with respect to the ambient air pressure outside the respirator.

## Slide 15: Definitions
Filtering Facepiece (Dust Mask)
A negative pressure particulate respirator with a filter as an integral part of the facepiece or with the entire facepiece composed of the filtering medium.

## Slide 16: Definitions
Air-Purifying Respirator (APR)
A respirator with an air-purifying filter, cartridge, or canister that removes specific air contaminants by passing ambient air through the air-purifying element.

## Slide 17: Definitions
Positive Pressure Respirator
A respirator in which the pressure inside the respiratory inlet covering exceeds the ambient air pressure outside the respirator.

## Slide 18: Definitions
Powered Air-Purifying Respirator (PAPR)
An air-purifying respirator that uses a blower to force the ambient air through air-purifying elements to the inlet covering.

## Slide 19: Definitions
Atmosphere-Supplying Respirator
A respirator that supplies the user with breathing air from a source independent of the ambient atmosphere
Includes supplied-air respirators (SARs) and self-contained breathing apparatus (SCBA) units

## Slide 20: Definitions
Classes of Atmosphere- Supplying Respirators
Continuous Flow
Demand
Pressure Demand

## Slide 21: Definitions
Supplied Air Respirator (SAR) or Airline Respirator
An atmosphere-supplying respirator for which the source of breathing air is not designed to be carried by the user.

## Slide 22
Definitions
Self-Contained Breathing Apparatus (SCBA)
An atmosphere-supplying respirator for which the breathing air source is designed to be carried by the user.

## Slide 23
Definitions
Escape-Only Respirator
A respirator intended to be used only for emergency exit

## Slide 24: Respirator Program
Written program - worksite-specific procedures
Must update program as necessary
Program administrator qualified person to administer the program
Must provide:
  Respirators
  Training
  Medical evaluations
  ……at no cost to the employee
Note: See Small Entity Compliance Guide

## Slide 25: Respirator Program Where Respirator Use is Not Required
Provide at employee’s request or permit employees to use their own respirators, if such use in itself will not create a hazard
Voluntary - provide users with the information contained in Appendix D
Establish and implement minimal elements of written program … ensure that:
  Medically able to use the respirator
  cleaned
  stored
  maintained so it does not present a health hazard to the user
Exception: Voluntary use of filtering facepieces (dust masks), are not required to be included in written program.

## Slide 26: Respirator Program Elements
1. Selection
2. Medical evaluation
3. Fit testing
4. Use
5. Maintenance and care
6. Breathing air quality and use
7. Training
8. Program evaluation

## Slide 27: Selection of Respirators
Selection based on hazards and factors that affect respirator performance and reliability

## Slide 28: Selection of Respirators
Types of Respirators
Facepiece (quarter, half, full)
Positive and Negative Pressure
Loose and Tight Fitting
Air Purifying (APR) and Air Supplied (SAR)

## Slide 29: Selection of Respirators
Types of Respirators
Half Mask Negative APR
Full Face Negative APR
PAPR Positive APR
SAR Positive SAR
  - SCBA
  - Bottled Air
  - Compressor

## Slide 30: Selection of Respirators
NIOSH-certified respirator - in compliance with the conditions of its certification
Identify and evaluate the respiratory hazards
Immediately Dangerous to Life or Health (IDLH)
Select respirators from a sufficient number of models and sizes

## Slide 31: Selection of Respirators
Immediately Dangerous to Life and Health (IDLH)
An atmosphere that poses an immediate threat to life, would cause irreversible adverse health effects, or would impair an individual’s ability to escape from a dangerous atmosphere.

## Slide 32: Selection of Respirators
Oxygen Deficient Atmosphere
An atmosphere with an oxygen content below 19.5% by volume
All oxygen deficient atmospheres are considered IDLH

## Slide 33
Respirators for IDLH Atmospheres
Full Facepiece Pressure Demand SCBA certified by NIOSH for a minimum service life of 30 minutes
Full Facepiece Pressure Demand SAR with Auxiliary Combination Self-Contained Air Supply
Selection of Respirators

## Slide 34: Respirators for IDLH Atmospheres (cont’d)
Respirators only for escape from IDLH atmospheres: NIOSH-certified for escape from the atmosphere in which they will be used.
Exception: Employers may use any atmosphere-supplying respirator, provided they can demonstrate, under all foreseeable conditions, that oxygen levels in the work area can be maintained between 19.5% and a lower value that corresponds to an altitude-adjusted oxygen partial pressure equivalent to 16% oxygen at sea level).
Selection of Respirators

## Slide 35: Selection of Respirators
Assigned Protection Factor (APF) - DEFINITION:
The workplace level of respiratory protection that a respirator or class of respirators is expected to provide to employees when the employer implements a continuing, effective respiratory protection program as specified in this section.

## Slide 36
Must use the APF’s listed in Table 1 (next slide)
Combination respirator (e.g., airline with an air-purifying filter), ensure APF is appropriate to the mode of operation
Selection of Respirators
Assigned Protection Factors (APF’s)

## Slide 37
TABLE 1 – ASSIGNED PROTECTION FACTORS5 |  |  |  |  | 
Respirator Type1, 2 | Quarter Mask | Half Mask | Full Face | Helmet/Hood | Loose-Fitting
Air Purifying | 5 | 310 | 50 | ----------------- | -----------------
PAPR | -------------------- | 50 | 1,000 | 425/1,000 | 25
SAR Demand Continuous Flow Pressure Demand/ other (+) pressure | -------------------- -------------------- -------------------- | 10 50 50 | 50 1,000 1,000 | --------------------- 425/1,000 --------------------- | -------------------- 25 --------------------
SCBA Demand Pressure Demand/ other (+) pressure | -------------------- -------------------- | 10 ------------------ | 50 10,000 | 50 10,000 | ----------------------------------------
1May use respirators assigned for higher concentrations in lower concentrations or when required use is independent of concentration.
2These APF’s are only effective when employer has a continuing, effective respirator program per 1910.134.
3This APF category includes filtering facepieces and elastomeric facepieces.
4Must have manufacturer test evidence to support an APF of 1,000 or else these respirators receive an APF of 25.
5These APFs do not apply to escape-only respirators. Escape respirators must conform to 1910.134(d)(2)(ii) or OSHA’s substance specific standards, if used with those substances.

## Slide 38
Maximum Use Concentration (MUC) - DEFINITION:
The maximum atmospheric concentration of a hazardous substance from which an employee can be expected to be protected when wearing a respirator, and is determined by the assigned protection factor of the respirator or class of respirators and the exposure limit of the hazardous substance
MUC = APF x OSHA Exposure Limit1
1 When an OSHA exposure limit is NOT available for a hazardous substance, the employer must determine an MUC on the basis of relevant available information and informed professional judgment.
Selection of Respirators

## Slide 39
Maximum Use Concentration (MUC)
Maintain exposure to the hazardous substance, when measured outside the respirator, at or below the MUC
MUCs do not apply to IDLH.
When calculated MUC exceeds the IDLH or the performance limits of the cartridge or canister, set maximum MUC at that lower limit
Select a respirator appropriate for the chemical state and physical form of the contaminant
Selection of Respirators

## Slide 40
Maximum Use Concentration - Example
What is the MUC for an employee wearing a half-mask air purifying respirator (APF=10) in an atmosphere of sulfur dioxide gas (PEL=5 ppm)?
MUC = APF x OSHA Exposure Limit
MUC = 10 x 5 ppm = 50 ppm
Note that this calculated value does not exceed the IDLH level for sulfur dioxide (100 ppm), so that the MUC for this example would be 50 ppm.
Selection of Respirators

## Slide 41
Respirators for Atmospheres NOT IDLH Gases and Vapors
Atmosphere-supplying respirator, or
Air-purifying respirator, if:
  End-of-Service-Life Indicator (ESLI)
  No ESLI create a change schedule based on objective information or data ensuring changed before the end of their service life
    Describe the information and data relied upon and basis for the change schedule and reliance on the data
Selection of Respirators

## Slide 42
For Particulate Exposures that are NOT IDLH
Employer must provide:
  an atmosphere-supplying respirator; or
  Air-purifying respirator equipped with HEPA filters certified by NIOSH under 30 CFR Part 11 or with filters certified for particulates under 42 CFR Part 84; or
  Air-purifying respirator equipped with any filter certified for particulates by NIOSH for contaminants consisting primarily of particles with mass median aerodynamic diameters of at least 2 micrometers
Selection of Respirators

## Slide 43: Selection of Respirators
Classes of Nonpowered Air-Purifying Particulate Filters:
Nine classes: Three levels of filter efficiency (%), each with three categories of resistance to filter efficiency degradation due to the presence of oil aerosols (NRP).
N R P
100 100 99 99 99 95 95 95
N for Not resistant to oil
R for Resistant to oil
P for oil Proof
Notes: - While Part 11 classifications were substance-specific (dust, fume, mist, etc.), Part 84 classifies particulate filters by efficiency and performance characteristics against non-oil and oil-containing hazards.
- There are nine classes of filters (three levels of filter efficiency, each with three categories of resistance to filter efficiency degradation).
- Levels of filter efficiency are 95%, 99%, and 99.97%.
- Categories of resistance to filter efficiency degradation are labeled N, R, and P.
- Use of the filter will be clearly marked on the filter, filter package, or respirator box (e.g., N95 means N-series filter at least 95% efficient).

## Slide 44: Selection of Respirators
N, R, P 100 is 99.7% efficient – N, R, P 95/99/100 clearly marked on box
If no oil particles are present, use any series (N, R, or P)
If oil particles are present, use only R or P series
If oil particles are present and the filter is to be used for more than one work shift, use only P series
Follow the respirator filter manufacturer’s service-time-limit recommendations

## Slide 45: Selection of Respirators
High Efficiency Filters
Filter >99.97% efficient - removing monodisperse particles of 0.3 micrometers in diameter. (HEPA filter per NIOSH 30 CFR 11)
Equivalent NIOSH 42 CFR 84 particulate filters are the N100, R100, and P100 filters.
Notes: NIOSH no longer uses the term “HEPA filter” in its new respirator certification standard (42 CFR 84). However, OSHA has retained this definition because it is used in many of the existing substance-specific standards. When HEPA filters are required by an OSHA standard, N100, R100, and P100 filters can be used to replace them.

## Slide 46: Medical Evaluation
Procedures
Must provide, before fit testing and use to determine employee’s ability to use a respirator
Must identify a PLHCP to perform medical evaluations
  medical questionnaire or
  an initial medical examination that obtains the same information

## Slide 47: Medical Evaluation
Procedures (c0n’t)
Medical evaluation must obtain the information requested by the questionnaire in Sections 1 and 2, Part A of App. C
Follow-up medical examination is required with
  Positive response to ANY question 1 through 8 in Section 2, Part A of App. C
  Initial medical examination demonstrates the need for a follow-up medical examination

## Slide 48: Medical Evaluation
Additional Medical Evaluations
Annual review of medical status is not required
At a minimum, employer must provide additional medical evaluations if:
  Employee reports medical signs or symptoms
  PLHCP, supervisor, or program administrator determines reevaluation needed
  Observations made during fit testing and program evaluation, indicates a need
  Change occurs in workplace conditions that may substantially increase the physiological burden on an employee

## Slide 49: Fit Testing
Before use of negative or positive pressure tight-fitting facepiece employee must be fit tested
- same make, model, style, and size of respirator that will be used.
The fit test must be administered using an OSHA-accepted Qualitative Fit Test (QLFT) or Quantitative Fit Test (QNFT) protocol contained in Appendix A

## Slide 50
Qualitative Fit Test (QLFT) - A pass/fail fit test to assess the adequacy of respirator fit that relies on the individual’s response to the test agent.
Fit Testing
  QLFT Protocols:
    Isoamyl acetate
    Saccharin
    Bitrex
    Irritant smoke

## Slide 51
Quantitative Fit Test (QNFT) - An assessment of the adequacy of respirator fit by numerically measuring the amount of leakage into the respirator.
Fit Testing
  QNFT Protocols:
    Generated Aerosol (corn oil, salt, DEHP)
    Condensation Nuclei Counter (CNC - PortaCount)
    Modified Condensed Nuclei Counter for Full/half mask elastomeric respirators (CNC – PortaCount) – different exercises
    Modified Condensed Nuclei Counter for Full/half mask elastomeric respirators (CNC – PortaCount) – different exercises
    Controlled Negative Pressure (Dynatech FitTester 3000)
    Controlled Negative Pressure (CNP) REDON

## Slide 52: Fit Testing
Employees using tight-fitting facepiece respirators must pass an appropriate (QLFT) or (QNFT):
  prior to initial use,
  whenever a different respirator facepiece is used, and
  at least annually thereafter
Additional fit test
  whenever the employee reports, or
  employer or PLHCP makes visual observations of, changes in the employee’s physical condition that could affect respirator fit

## Slide 53: Fit Testing
Fit Factor - A quantitative estimate of the fit of a particular respirator to a specific individual, and typically estimates the ratio:
Concentration of a substance in ambient air
Concentration inside the respirator when worn

## Slide 54: Fit Testing
QLFT may only be used to fit test negative pressure APRs that must achieve a fit factor < 100
The QNFT has been passed if the fit factor is
  >100 for tight-fitting half facepieces or
  > 500 for tight-fitting full facepieces,

## Slide 55: Use of Respirators
Facepiece Seal Protection – Tight-fitting respirators
NO facial hair or any condition that interferes with the face-to-facepiece seal or valve function
Corrective glasses or goggles or other PPE CANNOT interfere with the face-to-facepiece seal
Perform user seal check each time they put on the respirator – Follow Appendix B-1 or equivalent

## Slide 56: Use of Respirators
User Seal Check - An action conducted by the respirator user to determine if the respirator is properly seated to the face.

## Slide 57: Use of Respirators
Continuing Respirator Effectiveness
Survey work area conditions and degree of exposure or stress - reevaluate effectiveness if affected by changes
Employees must leave the respirator use area:
  to wash their faces and respirator facepieces as necessary
  to replace the respirator or filter, cartridge, or canister
  If vapor or gas breakthrough, changes in breathing resistance, or leakage of the facepiece
  …. And employer must replace or repair the respirator before allowing employee to return to the work area

## Slide 58: Use of Respirators
Procedures for IDLH Atmospheres
One or more employee(s) must be located outside the IDLH atmosphere
Maintain communication inside to outside - Visual, voice, or signal line
Effective emergency rescue - outside employee must be trained and equipped
Before emergency rescue – notify Employer or authorized designee
Employer or authorized designee, once notified, must provide necessary assistance appropriate to the situation

## Slide 59: Use of Respirators
Procedures for IDLH Atmospheres
Equip employees located outside the IDLH atmosphere with:
  a pressure demand or other positive pressure SCBA or SAR with auxiliary SCBA; and either
  appropriate retrieval equipment, where equipment would contribute to the rescue of employees and would not increase the overall risk resulting from entry; or
  equivalent means for rescue where retrieval equipment is not required per above

## Slide 60: Use of Respirators
Procedures for Interior Structural Firefighting:
> 2 employees must enter and remain in visual or voice contact with one another at all times
> 2 employees outside
Must use SCBAs
additional role (e.g., incident commander) - 1 employee located outside may be assigned but cannot interfere assistance or rescue activities
Does not preclude firefighters from performing emergency rescue before an entire team has assembled

## Slide 61: Maintenance and Care
Respirator must be clean, sanitary and good working order
Follow Appendix B-2 or equivalent manufacturer’s recommendations
Clean and disinfect:
  Exclusive use - as often as necessary
  Multiple users - before being worn by different user
  Emergency respirators - after each use
  Fit testing and training- after each use

## Slide 62: Breathing Air Quality and Use
Compressed breathing air must > ANSI/CGA G-7.1-1989. Type 1 - Grade D breathing:
  Oxygen content of 19.5 - 23.5%
  Hydrocarbon (condensed) content of 5 milligrams per cubic meter (mg/m3) of air or less
  CO < 10 parts per million (ppm)
  CO2 < 1,000 ppm
  Lack of noticeable odor

## Slide 63: Breathing Air Quality and Use
Compressors supplying breathing air equipped with:
  Suitable in-line air-purifying sorbent beds
  Filters that are maintained and replaced or refurbished per manufacturer’s instructions
Compressors not oil lubricated – Breathing air CO levels > 10 ppm
Oil-lubricated compressors require an alarmto monitor CO levels
  High-temperature or
  CO alarm, or both,
  NOTE: if only high-temperature alarms are used, the air supply must be monitored at sufficient intervals to prevent CO levels from exceeding 10 ppm

## Slide 64
Must be color-coded and labeled with NIOSH approval label
Label must not be removed and must remain legible
“TC number” is no longer on cartridges or filters (Part 84)
Marked with “NIOSH”, manufacturer’s name and part number, and an abbreviation to indicate cartridge or filter type (e.g., N95, P100, etc.)
Matrix approval label supplied, usually as insert in box
Identification of Filters, Cartridges, and Canisters

## Slide 65: Training and Information
Employers must provide effective training to employees who are required to use respirators.

## Slide 66: Training and Information
Must be able to demonstrate knowledge of at least:
  Why the respirator is necessary and how improper fit, use, or maintenance can compromise its protective effect
  Limitations and capabilities of the respirator
  Effective use in emergency situations
  How to inspect, put on and remove, use and check the seals
  Maintenance and storage
  Recognition of medical signs and symptoms that may limit or prevent effective use
  General requirements of this standard

## Slide 67: Training and Information
When to perform training:
Prior to use, unless acceptable training has been provided by another employer within the past 12 months
Retraining required annually, and when:
  changes in the workplace or type of respirator render previous training obsolete
  inadequacies in the employee’s knowledge or use
  any other situation arises in which retraining appears necessary
Voluntary use - Basic advisory information in Appendix D – provide to when use is not required by this standard or by the employer

## Slide 68: Program Evaluation
Conduct evaluations of the workplace as necessary to ensure effective implementation of the program
Must regularly consult employees required to use respirators to assess their views on program effectiveness and to identify and correct any problems
  factors to be assessed include, but are not limited to:
    respirator fit (including effect on workplace performance)
    appropriate selection
    proper use
    proper maintenance

## Slide 69: Recordkeeping
Records of medical evaluations must be retained and made available per 29 CFR 1910.1020
A record of fit tests must be established and retained until the next fit test is administered
A written copy of the current program must be retained
Written materials required to be retained must be made available upon request to affected employees and OSHA

## Slide 70: References
OSHA’s 1910.134 standard - https://www.osha.gov/laws-regs/regulations/standardnumber/1910/1910.134
OSHA’s Safety and Health Topics - Respiratory Protection - https://www.osha.gov/respiratory-protection
OSHA Small Entity Compliance Guide for the Respiratory Protection Standard – OSHA 3384-2011
NIOSH Respirator Selection Logic – U. S. Department of Health and Human Services, Centers for Disease Control and Prevention, National Institute for Occupational Safety and Health. October 2004
IUP, PA/OSHA Consultation Resources – Respiratory Protection 29 CFR 1910.134 Safety Training Presentation 2020
3M Occupational Health and Safety Division, MSA, North Safety Products and TSI for high contributing some of the graphics used in this program. Appearance of their products does not imply endorsement by IUP, PA/OSHA Consultation Program.
National Resource Center (Consortium), West Virginia University, Safety and Health Extension (Lead Organization). 3604 Collins Ferry Road P.O. Box 6615, Morgantown, WV www.wvusafetyandhealth.org
www.iup.edu/pa-oshaconsultation

## Slide 71
www.iup.edu/pa-oshaconsultation

## Slide 72: Contact us
Bryan B. Brougher
Brougher@iup.edu
Pennsylvania OSHA Consultation Office
Phone: 800-382-1241
Website: www.iup.edu/pa-oshaconsultation/
Facebook: https://www.facebook.com/Pennsylvania-OSHA-Consultation-Program-548810235234647/
Twitter: https://twitter.com/search?q=PA%20OSHA%20Consultation&src=savs
www.iup.edu/pa-oshaconsultation

## Slide 73: Thank You
Upcoming Webinar:
Beryllium & the OSHA Standard
October 5, 2022 @ 10:30am
Pennsylvania OSHA Consultation Office
Phone: 800-382-1241 or 724-357-4095
Website: www.iup.edu/pa-oshaconsultation
www.iup.edu/pa-oshaconsultation